## Slide 1
MR Defecography – Getting to the bottom of it
Dr Pavankumar, Department of Radio diagnosis, Aster CMI Hospital, Bangalore

## Slide 2
MR defecography – Normal Anatomy
Urinary bladder
Uterus
Vagina
Levator ani
Rectum
Anorectal junction
Anal canal

## Slide 3
MR defecography – Male pelvis anatomy
Puborectalis muscle
Rectum
Prostate

## Slide 4
Abnormalities to asses
Rectocele.
Vaginocele.
Cystocele.
Global pelvic weakness.
Omentocele.
Enterocele.
Rectal intussuception.
Clinical features
Constipation
Incomplete defecation
Ansimus
Prolapse

## Slide 5
MR Defecography – Procedure requirements
MR machine
Body coil
Gel bottle
Tube
Diaper

## Slide 6
Patient preperation
No patient preparation required
150ml of ultrasound gel is inserted per rectum.
Sequences – Axial, coronal and sagittal T2W and dynamic sequences

## Slide 7
Rest
Squeeze
Strain
Defecate
Dynamic sequences are acquired in 4 of the following steps/stages

## Slide 8
Puborectalis
Rectum
Anal canal
Pubic bone
First phase – Rest
Diagramatic representation
Static image in rest phase
Dynamic MR/video in rest phase

## Slide 9
Puborectalis
Pubic bone
Rectum
Anal canal
Second phase – Squeeze
Diagramatic representation
Static image in squeeze phase
Dynamic MR/video in squeeze phase

## Slide 10
Puborectalis
Rectum
Anal canal
Pubic bone
Third phase – Strain
Diagramatic representation
Static image in strain phase
Dynamic MR/video in strain phase

## Slide 11
Puborectalis
Pubic bone
Rectum
Anal canal
Fourth phase – Defecation
Diagramatic representation
Static image in defecation phase
Dynamic MR/video in defecation phase
Mild rectal prolapse with Medium sized anterior rectocele

## Slide 12
Measurements
Pubococcygeal line – A line joining the inferior aspect of pubic symphysis to the last coccygeal joint.
H line – Corresponds to the AP diameter of the Hiatus.
M line – Perpendicular distance between the pubococcygeal line and posterior anorectal junction.

## Slide 13
Measurements
Anorectal angle –
Formed by a line passing through the centre of anal canal and a line passing along the posterior wall of rectum.
At rest – 100- 127.
Decreases – During Squeeze.
Increases – During strain / Defecation.

## Slide 14
Staging pelvic organ prolapse based on pubococcygeal line
Small organ prolapse
Medium organ prolapse
Large organ prolapse
Less than 3cm caudal to PCL line
3-6 cm caudal to PCL line
>6cm caudal to PCL line
Stage Measurement
Anterior Rectocele – Ventral prolapse of rectum for more than 2cm.
Classification –
Mild - <2cm.
Moderate – 2-4cm.
Severe - >4cm.

## Slide 15
Case I – 54 year old female with dysynergic defecation.
Findings – Mild Rectal prolapse with (2.9cm) with large anterior rectocele(3.4cm).
Rest Squeeze Strain Defecate

## Slide 16
Case II – 67 Year old male with altered bowel movements and mass per rectum
Findings – Small rectal prolapse during strain and defecation phase (<2cm).
Rest Squeeze Strain Defecate
Hydrocele

## Slide 17
Rest Squeeze Strain Defecate
Case III – 37 Year old male with difficulty in passing stools.
Findings – Moderate Rectal prolapse with (5.6cm) with small anterior rectocele.
3
Rectocele

## Slide 18
Case IV –61 year old female presented with history of constipation.
Findings – Global pelvic floor weakness, moderate Rectal prolapse with rectocele and cystocele.
Rest Squeeze Strain Defecate

## Slide 19
Case V –25 year old female presented with history of constipation.
Findings – Global pelvic floor weakness with large rectal prolapse, uterine/vaginal prolapse, moderate cystocele and enterocele.
Rest Squeeze Strain Defecate

## Slide 20
Conclusion
No use of intravenous contrast and ionizing radiation.
It is superior to fluoroscopic defecography in providing the ability to detect associated abnormalities in the bladder and cervix/vagina.
Real time imaging- Providing dynamic evaluation of position of different structure in different phases.
The exam is fast (approx. 30 minutes).
Grading of severity of pelvic floor weakness and organ descent.